## Slide 1: Autogas Infrastructure Simple, Scalable, and Affordable
Brian Green
Green’s Blue Flame Gas Company

## Slide 2: Autogas Infrastructure Components
Tank
Skid/structure
Plumbing
Pump
Fill Nozzle and Hose
Dispenser
Other Requirements:
- Site Preparation
- Power Supply
- Crash Protection

## Slide 3: Dispensers and Operation
Simple Access - Push to Start
Card Access
  Cellular based communication
  Customizable data management
  Accommodate multiple fleets at a single location
Single or Dual Hose Set-ups
Installed with hose, nozzle, and, break-away device
Dispensers can be added as your propane fleet grows

## Slide 4: Nozzles
ACME Low Emission
  Standard in the propane industry for decades
  Connects using ACME Threads
  1.9 cc product released
Ultra-Low Emission Quick Connection
  Only 0.4 cc product released
  Locks when the trigger is pulled
  Unlocks automatically then trigger is released
  Propane does not flow unless properly connected
Funding is available to switch to Ultra-Low Emission Nozzle
  $100 per tank-side connector, $1,000 hose-end

## Slide 5: Tank Options – Flexible and Scalable
Horizontal
  Preferred option – cost/availability
  1,000 gallon/2,000 gallon +
  Additional tanks can be added as your propane fleet grows
  Tanks are monitored remotely using a cellular device
    Sends emails and texts to operations staff when thresholds are met

## Slide 6: Tank Options – Flexible and Scalable
Vertical
  Best option when space is constrained
  Cost about 4-5X more than horizontal tanks to purchase and install
  Offered in ranges of 660-2000 gallons
  X-Base and rails available for retro-fit installations

## Slide 7: Tank Options – Flexible and Scalable
Large Volume
  Long term commitment w/ large fleet (School Districts)
  18,000/30,000 gallons
  Largest cost to install - Largest cost savings on fuel
    Transport Delivery
  Redundancy usually built into these installations
    Multiple dispensers, dual pumps, etc.
Installation for Clear Creek ISD by Propane Specialty Services

## Slide 8: Site Requirements for Autogas Infrastructure
Concrete/Structural
  6” concrete pads for most tank installations
  Concrete forms for 18,000+ gallon tanks
Electrical
  Pump – 240V power supply
  Dispenser – 120V power supply
  Emergency shut down valve
Crash Protection
  Bollards or crash posts and rails per Texas Railroad Commission requirements

## Slide 9: Autogas Infrastructure Costs
Purchase tank and dispensing equipment
  1000 gallon horizontal tank and dispenser on skid
    ~$45-60k depending on dispenser and current site
  18,000 gallon tank with multiple dispensers and redundant pumps
    ~$250-300k
Lease tank and dispensing equipment from propane provider
  Costs for propane equipment (tanks, pump, dispenser, etc.)
    $0
  Costs for site preparation, electrical, and crash protection
    $5-15k

## Slide 10: Propane Mowers
Propane is a great fuel for commercial landscaping!
Wide variety of propane conversions and mowers available from OEMs
  John Deere, Exmark, Bobcat, Wright, Gravely, Toro…
Refueling Options
  Cylinder re-fuel/exchange or dispensing systems
30%+ savings in fuel costs
Bonus: Savings on refueling time
Many landscapers start using propane fleet vehicles also

## Slide 11: Questions
Brian Green
713-562-8852
brian@greensblueflame.com